## Slide 1
WISE: Low-Cost Wide Band Spectrum Sensing Using UWB
Zhicheng Luo1,3, Qianyi Huang2,3, Rui Wang1, Hao Chen3, Xiaofeng Tao4,3, Guihai Chen5, Qian Zhang6
Southern University of Science and Technology1, Sun Yat-sen University2,
Peng Cheng Laboratory3, Beijing University of Posts and Telecommunications4,
Shanghai Jiao Tong University5, Hong Kong University of Science and Technology6
Notes: Hello everyone, I am Zhicheng. Today I will introduce our work: WISE low-cost wide band spectrum sensing using UWB.

## Slide 2
Shortage of Spectrum Resource
Spectrum shortage is coming
The number of wireless devices is growing rapidly
2027
36.4
2017
2022
4.7
26.4
Billion
Year
Conventional Spectrum Access
Spectrum
......
Access
Notes: Now, the number of wireless devices is growing rapidly and \ thus resulting in a shortage of spectrum resources.

## Slide 3
Primary users
Dynamic Spectrum Access (DSA)
Spectrum
Spectrum sensing
Access
Access
Secondary users
City-level wideband (150MHz ~ 1GHz) spectrum sensor is in need
Notes: The FCC has proposed Dynamic Spectrum Access (DSA), which \ allows primary users and secondary users to share the same spectrum band. The \ secondary users can use the spectrum band when the primary users are idle. The key point for the success of DSA \ is the wideband spectrum sensing capability.

## Slide 4
City-level wideband (150MHz ~ 1GHz) spectrum sensor is in need
Unlicensed Bands
CBRS band,
150MHz (From 3.55GHz to 3.70GHz)
Unlicensed 6GHz band
1.2GHz (From5.925 GHz to 7.125GHz)
Notes: FCC has released 150MHz and 1.2GHz unlicensed spectrum for dynamic spectrum access in 3.5GHz and 6GHz, respectively. / Thus, a low-cost wideband spectrum sensor is in need.

## Slide 5
S3
RTL-Dongle
SweepSense
Wideband Spectrum Sensing
Low time resolution
Not ready for large scale deployment
Notes: However, although there is some existing works on wideband spectrum sensing, the prior work has some limitations \ such as low time resolution or \ not ready for large scale deployment.

## Slide 6
Can we enable wideband spectrum monitoring with low-cost, commercial off-the-shelf devices?
WISE：Low-Cost Wide Band Spectrum Sensing Using UWB
Notes: So, we ask the question that, can we enable wideband spectrum monitoring with low-cost, commercial off-the-shelf devices? \ In this work, we design WISE, a Low-cost wide band spectrum sensor using UWB.

## Slide 7
Preamble p(t)
Data
PHR
Feasibility of Spectrum Sensing
h(t)
p(t)*h(t)
Correlation
Preamble p(t)
FFT
H(f)(CFR)
h(t)(CIR)
Notes: In UWB communications, the transmitter will \ transmit a known preamble signal to the receiver, who \ will correlate the received signal with the preamble signal and \ calculate the channel impulse response (CIR). \ After FFT operation, we will get the channel frequency response (CFR). We define it as H(f)

## Slide 8
Preamble p(t)
Data
PHR
Feasibility of Spectrum Sensing
h(t)
(p(t)+x(t))*h(t)
Single-tone signal x(t)
p(t)*h(t)
FFT
H(f)+P(f)X(f)
Correlation
Preamble p(t)
h(t)(CIR)
H(f)(CFR)
h(t)+p(t)*x(t)
Notes: When there is another signal in the air, the receiver will \ also receive it, correlate \ it with the preamble and \ calculate the CFR.

## Slide 9
Feasibility of Spectrum Sensing
Preamble p(t)
Data
PHR
h(t)
(p(t)+x(t))*h(t)
Single-tone signal x(t)
FFT
Correlation
Preamble p(t)
h(t)+p(t)*x(t)
H(f)+P(f)X(f)
Notes: And~

## Slide 10
Feasibility of Spectrum Sensing

## Slide 11
H’(f)=H(f)+P(f)X(f)
Feasibility of Spectrum Sensing
900MHz
P(f)X(f)
H(f)
H’(f)=P(f)X(f)
Notes: In this CFR, it has both the external in-air signal response X(f) and internal response H(f). \ So, if we can remove the H(f) from the CFR, we can get the spectrum information of in-air signal. \ As the UWB has a maximum receiving bandwidth of 900MHz, we can sense up to 900MHz bandwidth in one detection.

## Slide 12
How to address the nature limitations of low-cost devices
  Low SPI speed
  Low spectral resolution
Challenges
How to extract the in-air signals
  Unknown AGC factor
  Non-predictable signal power
How to extract the in-air signals
Notes: Although it sounds straightforward, we face two challenges. The first challenge is how to extract the in-air signal and the second challenge is how to address the nature limitations of low-cost devices. \ For the first challenge,

## Slide 13
H’(f)=H(f)+P(f) ⋅X(f)
H’(f)=H(f)+P(f) ⋅X(f)
Constants
Controller
Excitation block
Receiving block
Sensing antenna
Extract the In-air Signals - Wired Connection
In-air signal source
CFR
✔
✔
Preamble p(t)
Notes: In System design, we use a \ sensing antenna to receive the external in-air signal, and use a wire\ to connect the UWB transmitter and \ receivers. The UWB transmitter will \ transmit a preamble as a trigger for measurement. The UWB receivers \ will calculate the CFR only when the preamble has been detected. \ In the wired connection, the H(f) and P(f) could be assumed as Constants.

## Slide 14
H(f)
Extract the In-air Signals - AGC
H’1(f)
H’2(f)
Notes: when we know the H(f), can we directly remove H(f) to calculate the in-air signal? the answer is no, For example, we \ have captured two in-air signals, the CFR is H1(f) and H2(f)。

## Slide 15
H(f)
H(f)
H(f)
Extract the In-air Signals - AGC
H’1(f)
H’2(f)
Notes: If we directly remove the H(f), the SNR will be too low to detect the in-air signal

## Slide 16
SNR is too low
H(f)
H(f)
H(f)
X1(f)=H’(f)-H(f)
X2(f)=H’(f)-H(f)
Extract the In-air Signals - AGC
H’1(f)
H’2(f)
X1(f)
X2(f)
Notes: If we directly remove the H(f), the SNR will be too low to detect the in-air signal

## Slide 17
H(f)
X2(f)=H’(f)-H(f)
X1(f)=H’(f)-H(f)
k1⋅H(f)
k2⋅H(f)
How to know k1 and k2?
Extract the In-air Signals - AGC
H’1(f)
H’2(f)
Notes: This is because the AGC will dynamically adjust the receiver gain to ensure optimal receiver performance. So, we need to figure out the unknown AGC factor before removing H(f)

## Slide 18
Polynomial fitting
  Unknown AGC factor - AGC calibration
AGC factor = F(f)/H(f)
AGC factor = F(f)/H(f)
F(f)
F(f)
Spikes
Spikes
--Result: F(f)
Notes: To figure out the AGC factor, we observe \ that the X(f) has more spikes in the frequency domain. Thus, we can use a low-degree polynomial(pɑli'noʊmiəl]) \ to fit the more smooth H(f), and \ the fitting result is F(f), we can \ calculate the AGC factor as ratio ([ˈreɪʃioʊ]) of H(f) to F(f), and then \ we can calculate X(f) by removing H(f)

## Slide 19
Detect preamble: SNR of preamble = Power of p(t) / Power of x(t)
Detect in-air signal: SNR of in-air signal = Power of x(t) / Power of p(t)
Low SNR
Fail to detect in-air signal
Low SNR
Fail to detect preamble
Preamble power:
-56.3dBm/MHz
Non-predictable Signal Power
Notes: In every measurement, we \ need to detect\ both the internal preamble and external in-air signal. However, as the \ power of external in-air signal is uncontrollable, when the power of external in-air signal is \ too weak compared with internal preamble, the external signal will be buried by the internal preamble; when it is \ too strong, the receiver will ignore the preamble and will not trigger the CIR estimation.

## Slide 20
Preamble power:
-56.3dBm/MHz
Preamble power:
-86.3dBm/MHz
-75dBm ~ -25dBm
State 1
State 2
Non-predictable Signal Power-Dynamic TX power control
Notes: To have a wide dynamic range, \ WISE has 2 levels of transmit power, and \ switches between those two levels\ according to the power of external in-air signal. Then we could detect signals with \ power from -75dBm to -25 dBm

## Slide 21
How to address the nature limitations of low-cost devices
  Low SPI speed
  Low spectral resolution
Challenges
How to extract the in-air signals
  Unknown AGC factor
  Non-predictable signal power
How to extract the in-air signals
How to address the nature limitations of low-cost devices
Notes: For now, we can detect the in-air signal. However, we still need to address the nature limitations of low-cost devices.

## Slide 22
low SPI speed - Radar mode
Time
1ms
Reading 1016 CIR points (2ms)
Sensing (64us)
Missing
Detection
Reading 150 CIR points (500us)
Normal mode
Radar mode
Radar(t)
Time interval: δ
Notes: The low-speed SPI interface will \ take about 2ms to fetch the complete CIR. This will \ lead to missing some fleeting signal like radar during the data communication time. In order to reduce the data communication time, instead of getting the complete CIR, each time \ we fetch only a portion of CIR, and design an inter-packet time interval to make sure WISE can capture at least one radar pulse in its sensing period.

## Slide 23
CFRs with low resolution
IFFT
CIRs
Low resolution-CIR concatenation
Zoom
Discontinuity
Spectral leakage
Splicing
Notes: The other limitation is low spectral resolution. To address this limitation, we try to \ concatenate several successive CIRs. The \ discontinuity in the time domain will lead to spectral leakage. We perform \ normalization and splicing and finally get a fine-grained spectrum

## Slide 24
Evaluation - Implementation
Testbed
WISE prototype
5G signal testing
Complex environment
Notes: This is the WISE prototype, we test WISE’s ability to detect wireless signals (including 5G), and evaluate its performance in complex environment.

## Slide 25
Evaluation - Comprehensive Performance
Error rate (FNR+FNR) =0.35%
Power estimation error<3dB
Notes: Here are some results, we can see that the Error rate is only 0.35%. The power estimation error is less than 3dB

## Slide 26
Evaluation - 5G Signal Detection
Spectrum of 5G signal
Monitoring 5G signal energy during downloading
Notes: WISE can also detect 5g signal and could be used to monitor 5G NR bands

## Slide 27
Evaluation - Robustness
Radar signal detection
Stable estimation in complex environment
Notes: WISE can detect radar signals, and can also work in complex environments

## Slide 28
Conclusion
We design WISE, a low-cost spectrum sensor that supports up to 900MHz bandwidth with high accuracy, good sensitivity, and wide dynamic range.
WISE can achieve good accuracy of 99.65% in busy channel detection. WISE can also estimate 5G signal power with error less than 3dB in a complex environment.
We demonstrate the spectrum sensing capability of UWB chips, which provide a new direction to build cheap and wideband spectrum sensors.
WISE can also detect fleeting radar signals and has good ability to detect 5G signals. WISE can be widely deployed and used for city-level spectrum planning.
Notes: In conclusion, we design WISE, a low-cost wideband spectrum sensor that can achieve good accuracy of 99.65% in channel occupation detection and can also estimate 5G signal power with less than 3dB error in complex environments. More details can be found in our paper. Thank you all for your attention.